## Slide 1: Towards Emulation of the BBC Micro Computer

## Slide 2: Some History
BBC Computer Literacy Project
Launched 1981
Manufactured by Acorn
2 MHz MOS Technology 6502/6512
RAM 16–32 KiB
Graphics - 6845 CRTC
  8 Modes
  160 × 256 8 Colours 640 × 256 1 Colours, Teletext
Sound – Texas Instruments SN76489

## Slide 3: Expansion

## Slide 4: Software - Games
Elite
Pacman (Snapper)
Frogger (Hopper)
Defender (Planetoid)
Centipede (Bug Blaster)
Asteroids (Meteors)

## Slide 5: Software - other
Languages (ROMS)
  Basic, Pascal, Forth, BCPL, LISP, Logo/Turtle graphics
Business
  Word processors (Wordwise), Spreadsheet (ViewSheet), Accounting, Database
Educational
  Maths, Physics, Electronics, Geography, Chemistry

## Slide 6: An Emulator you say…
Allows software written for one type of computer to run without modification on another…
… by recreating the hardware of the old system as software on the new system

## Slide 7: Stage 1
#3 Basic I/O
#2 Memory
#1 CPU
#4 Basic image loading
#5 OS call Interception

## Slide 8: The 6502 Microprocessor
Clock speed – 2 MHz
Transistors - ~3500
Buses
  Data – 8 bit
  Address – 16 bit => 64K address space
Registers
  1 Program counter (PC) 16 bit
  1 Stack pointer (S) 8 bit => 256 byte hardware stack!
  1 Status register (P)
  1 Accumulator (A) 8 bit
  2 Index registers (X,Y) 8 bit

## Slide 9: Aside – comparison with a modern system
 | BBC (6502) | Modern Desktop (Intel) | Comment
Clock speed | 2 MHz | 4 GHz | x2,000
Size | 21 mm2 | 100 mm2 | x5
Transistors | 2500 | 16,000,000,000 | x6,400,000
Fabrication | 8 µm | 5 nm | ~1000
Word size | 1 Byte | 8 Bytes | x8
Cores | 1 | 4(8)+ | x4(x8)
L1/L2/L3 cache | 0 | 64K/256K/2M x 4 | -
Memory | 32K | 32G | x1,000,000

## Slide 10: Programming the CPU
When you run any application, this is the code the computer is actually executing!
Lowest level of software
Binary language processed directly by the CPU
Simple instructions
  Load a value in to register
  Jump to an address
  Add two numbers
  Branch depending on value of status flag
Machine Code

## Slide 11: Structure of an Instruction
OpCode => What to do
Operand => What act on
Addressing mode => How to resolve the operand
Encoded together in 1 byte
0 to 3 byte depending on addressing mode
Load a value into the Accumulator
You’ll find the address of the value to load in the next two bytes
The address of the value to load

## Slide 12: Programming the CPU
Human readable form of machine code
1:1 correspondence with machine code
  This is NOT a higher-level language
An assembler translates assembly language into machine code for execution
Assembly Language
Op code
Label
Operand & addressing mode

## Slide 13: 6502 MC/Assembly Language
Implicit - CLC
Accumulator – LSR A
Immediate – LDA #10
Zero-page – LDX $10
Zero-page, X – AND $20, X
Zero-page, Y – STX $30, Y
Relative – BEQ $26
Absolute – JMP $20FE
Absolute, X – STA $3000, X
Absolute, Y – AND $2000, Y
Indirect - JMP ($FFCC)
Indexed Indirect - LDA ($40), A
Indirect Indexed – LDA ($40, A)
13 Addressing Modes
56 Op Codes
CLC – Clear the Carry flag
LDA – Load accumulator
INX – Increase X
ADC – Add to the accumulator
BEQ – Branch if Zero flag is set
ROR – Rotate bits right
JSR – Jump to a subroutine

## Slide 14: Tool Chain & Execution Process
6502 Emu
Memory
Basic I/O
Image loader
Keyboard
Screen
6502 Emulator
LDA ($00),Y
BEQ $07
Assembly Language
$B1 $00
$F0 $07
Machine Code
6502 cross assembler

## Slide 15: 6502 Debugger
Disassembly
Command output
Processor Registers
Memory writes
Hardware stack
Programme output
Load DASM images
Load core dumps
Single step
Step over
Disassembly
Memory inspection
Set reg/mem
Break points
Run until RTS
Functions

## Slide 16: Demo #1 – 6502 Emu & Debugger

## Slide 17: Stage 2 – From 6502 to BBC Micro (partial emulation)
#3 Paged ROM loading
#2 OS ROM loading
#1 6845 CTC Simple Mode 7
#5 Execution of BBC BASIC programmes
#4 OS Boot

## Slide 18: BBC Micro Emulation
OS ROM
BBC Basic ROM
6502 Emulator
Memory Mapped Screen
6845 CRTC Emulator
Working Memory
$BFFF
0xC000
0xFFFF
$8000
$0000
$7C00
$7FFF
$7FFF
Render
>
Mode 7 (Teletext)
Scan
JMP (0xFFFC)
Boot/6502 Reset
10 REM Input a number
20 REPEAT
30 PRINT “Enter "
40 INPUT N
50 UNTIL N >= 0 AND N <= 9
60 PRINT "Thank You"
BBC Basic Programme

## Slide 19: Demo 2 – Simple BBC Emu

## Slide 20: Status & What's Next
From the BBC Microcomputer Advanced User Guide
Done
Required
Unsure

## Slide 21
?