## Slide 1: Towards Emulation of the BBC Micro Computer

## Slide 2: Some History
BBC Computer Literacy Project
Launched 1981
Manufactured by Acorn
2 MHz MOS Technology 6502/6512
RAM 16–32 KiB
Graphics - 6845 CRTC
  8 Modes
  160 × 256 8 Colours 640 × 256 1 Colours, Teletext
Sound – Texas Instruments SN76489 ADSL

## Slide 3: Expansion

## Slide 4: Software - Games
Elite
Pacman (Snapper)
Frogger (Hopper)
Defender (Planetoid)
Centipede (Bug Blaster)
Asteroids (Meteors)

## Slide 5: Software - other
Languages (ROMS)
  Basic, Pascal, Forth, BCPL, LISP, Logo/Turtle graphics
Business
  Word processors (Wordwise), Spreadsheet (ViewSheet), Accounting, Database
Educational
  Maths, Physics, Electronics, Geography, Chemistry

## Slide 6: An Emulator you say…
Allows software written for one type of computer to run without modification on another…
… by recreating the hardware of the old system as software on the new system

## Slide 7: Step 1
CPU
Basic I/O
Memory

## Slide 8: The 6502 Microprocessor
Clock speed – 2 MHz
Transistors - ~3500
Buses
  Data – 8 bit
  Address – 16 bit => 64K address space
Registers
  1 Program counter (PC) 16 bit
  1 Stack pointer (S) 8 bit => 256 byte stack!
  1 Status register (P)
  1 Accumulator (A) 8 bit
  2 Index registers (X,Y) 8 bit

## Slide 9: Programming the CPU
When you run any application this is the code the computer is actually running!
Lowest level of software
Binary language processed directly by the CPU
Simple instructions
  Load a value in to register
  Jump to an address
  Add two numbers
  Branch depending on value of status flag
Machine Code

## Slide 10: Structure of an Instruction
OpCode => What to do
Operand => What act on
Addressing mode => How to resolve the operand
Encoded together in 1 byte
0 to 3 byte depending on addressing mode
Load a value into the Accumulator
You’ll find the address of the value to load in the next two bytes
The address of the value to load

## Slide 11: Programming the CPU
Assembly Language
Human readable form of machine code
1:1 correspondence with machine code
  This is NOT a higher-level language
An assembler translates assembly language into machine code for execution
Op code
Label
Operand & addressing mode

## Slide 12: 6502 MC/Assembly Language
Implicit - CLC
Accumulator – LSR A
Immediate – LDA #10
Zero page – LDX $10
Zero page, X – AND $20, X
Zero page, Y – STX $30, Y
Relative – BEQ $26
Absolute – JMP $20FE
Absolute, X – STA $3000, X
Absolute, Y – AND $2000, Y
Indirect - JMP ($FFCC)
Indexed Indirect - LDA ($40), A
Indirect Indexed – LDA ($40, A)
56 Op Codes
13 Addressing Modes
CLC – Clear the Carry flag
LDA – Load accumulator
INX – Increase X
ADC – Add to the accumulator
BEQ – Branch if Zero flag is set
ROR – Rotate bits right
JSR – Jump to a subroutine

## Slide 13: Execution Process

## Slide 14: Aside – comparison with a modern system

## Slide 15: …
Assembly language primer
Tool chain – assembler
Implemented functionality
OS interception
… features
Pull from readme
Internal architecture
Show example of translation

## Slide 16
Registers
Current instruction
Emulator messages
Program output
Single step
Run to completion
Dump core
Exit

## Slide 17
From the BBC Microcomputer Advanced User Guide
Done
Required
Unsure